## Slide 1
01
THE PROBLEM
Six in ten kilometres have no usable service
7,144 measurements, two days, 178 km² of Iowa farmland — served by one tower
SAMPLES
7,144
one every 2.6 s
NO SERVING CELL
42.3%
3,023 rows
ROUTE DRIVEN
117 km
distinct road
SURVEY BOX
178 km²
11.0 × 16.2 km
Every measurement, coloured by whether it had service
Chart: 
Service collapses with distance from the tower
Chart: 
| 0-2 km | 2-4 km | 4-6 km | 6-8 km | 8-13 km
% of samples with no cell | 6.3004 | 36.2647 | 48.7719 | 46.6667 | 66.8047
Downlink holds. Uplink does not.
Chart: 
| 0-2 km | 2-4 km | 4-6 km | 6-8 km | 8-13 km
downlink Mbps | 232 | 232 | 216.5 | 204.5 | 191
uplink Mbps | 62.9 | 52.4 | 31.5 | 15.25 | 10.5
Where does one more installation go? The tower sits 1.6 km from the north edge and 9.5 km from the south — the survey reaches six times further south than north.

## Slide 2
02
WHY IT IS HARD · 1 OF 2
Between 2 and 6 km, dead spots are terrain
Obstruction of the first Fresnel zone — not blocked line of sight
120 ft mast
first Fresnel zone
ridge clips the zone
receiver
Line of sight is clear. The link is still obstructed.
Outage rate, split by whether the path is obstructed
Chart: 
| 0-2 km | 2-4 km | 4-6 km | 6-8 km | 8-13 km
path clear | 5.9368 | 32.5026 | 41.1202 | 49.9096 | 67.3469
Fresnel obstructed | 13.2353 | 51.9481 | 62.5 | 45.1747 | 66.6905
BLOCKED LINE OF SIGHT
13%
of all links
INSIDE THE FRESNEL ZONE
46%
the real test
ODDS OF OUTAGE, 2-4 KM
2.25×
p = 7.7e-08
ODDS OF OUTAGE, 4-6 KM
2.39×
p = 5.5e-12
BEYOND 6 KM
no effect
link budget is gone
Obstructed cells are twice as likely to be dead as clear cells the same distance out. Past 6 km the effect vanishes — everything fails there anyway.
Terrain relief across the survey: 98 m. DEM: USGS 3DEP 1/3 arc-second, 10 m posts.

## Slide 3
03
HOW WE MODEL IT — AND WHAT WE CHECKED
One physical chain, and an honest account of where it holds
Geometry to received power to service, then tested against the measurements it did not see
GEOMETRY
distance, bearing, terrain profile
RSRP
path loss + knife-edge diffraction
AVAILABILITY
fitted curve, P(service) vs RSRP
COVERAGE
route-km 70% area 30%
The first two links are strong. The third is not.
Terrain absorbs a fifth of the scatter
Chart: 
| distance + azimuth | + terrain diffraction
residual σ, dB | 9.21 | 7.3464
and the exponent falls to free space
Chart: 
| without terrain | with terrain | free space
path-loss exponent | 2.4 | 1.8 | 2
RSRP error, three ways of splitting the data
Chart: 
| in sample | random split | held-out geography
MAE, dB | 5.5936 | 5.6049 | 7.6294
DIFFRACTION COEFFICIENT
-0.73
dB per dB · physics says −1
RSRP HELD-OUT R²
+0.15
vs +0.79 on a random split
AVAILABILITY, OUR MODEL
59%
base rate is 64%
WHERE VS WHEN
71 / 5%
of outage variance
What the backtest says: the propagation model is sound, the availability step is weak. Received power we predict to 5.9 dB; whether a cell has service we barely beat guessing. So the device comparison holds and the absolute coverage percentages do not.

## Slide 4
04
WHY IT IS HARD · 2 OF 2
No device on the menu can reach
Every 6 dB of transmit power lost halves the radius and quarters the area
Service radius, drawn to scale
Macro 5,036 m
Relay 390 m
Small cell 181 m
 | Macro-class | Donor relay | Small cell
Power vs the tower | same | −20 dB | −26 dB
Mast height | 37 m | 10 m | 10 m
Backhaul | fibre + tower | over the air | fibre
Service radius | 5,036 m | 390 m | 181 m
Coverage area | 1.00× | 0.009× | 0.002×
Gain collapses with transmit power
Chart: 
| −0 | −5 | −10 | −15 | −20 | −26 | −32
coverage gain | 0.56509 | 0.47528 | 0.3339 | 0.28457 | 0.19555 | 0.023663 | 0.0024406
What one of each actually adds
Chart: 
| route-km added | km² added
Macro | 28.625 | 42.64
Relay | 1.375 | 0.48
Small cell | 0.7 | 0.08
5 dB below the tower halves the gain. 10 dB cuts it to a sixth. A relay is 20 dB down — a 520 m bubble against a 9 km hole.

## Slide 5
05
WHY OUR SOLUTION WORKS · THE TOOL
Everything the brief asks for, in one clickable page
Click anywhere and the terrain model re-solves the whole surface, live in the browser
YOUR SITE
existing tower
click to place · drag to pan · scroll to zoom
The brief asks for four things. Each is a tab.
Thresholds
before / after at four explicit service definitions
Robustness
150 fresh shadow-fading draws, run live on the placed site
Gains
per device class, and per successive installation
Sensitivity
gain swept against mast height and transmit power
Nothing is a stored answer — the page carries the terrain model and runs the same physics as the offline optimiser, matching it to about 1%.
TERRAIN POSTS CARRIED
31 m
3DEP, 501 × 851 grid
DEMAND CELLS RE-SOLVED
4,731
on every click
AGREEMENT WITH THE OPTIMISER
~1%
verified against the offline run
EXTERNAL DEPENDENCIES
none
one file, opens anywhere

## Slide 6
06
THE ANSWER
One macro-class site, 6.5 km south-west
What one installation of each class can and cannot do
Route coverage after one installation
Chart: 
| now | + small cell | + relay | + macro
% of route-km served | 44.4492 | 45.0493 | 45.6279 | 68.9884
Under four explicit service thresholds
available | route now | after | area now | after
≥25% | 96.8% | 100.0% | 93.0% | 100.0%
≥50% | 44.4% | 99.5% | 36.8% | 96.7%
≥75% | 10.1% | 55.5% | 6.2% | 51.5%
≥90% | 3.5% | 36.0% | 2.0% | 29.8%
THE ONE THAT WORKS
Macro-class site, 6.5 km south-west
41.97956, −93.82983 · 37 m mast · on the road network
40% → 65% of route · 34% → 56% of area · 1,079 dead cells fixed
Gain over 400 shadow-fading draws
Chart: 
| p10 | median | p90
coverage gain | 0.47794 | 0.49234 | 0.50556
DRAWS WITH A POSITIVE GAIN
100%
the site is never a mistake
RELAY
+1.4 pts
520 m radius
SMALL CELL
+0.9 pts
256 m radius
STILL UNCOVERED
35%
of route — needs a programme
Read the ratios, not the absolutes. The device comparison rests on the fitted path-loss law; the percentages inherit a weak availability step that the backtest showed barely beats the base rate.