## Slide 1
Arathon Challenge 03
Where should the next tower go?
Rural network planning on 7% of the map
Four towers serve this area today, and most of it still has no usable signal — 42% of the samples the van took found no cell at all. One more asset could change that. The question is where to put it.
Red is where service fails today. The star is where our planner would put the next tower.
UNSERVED TODAY
60%
of the area, by our model
WE MEASURED
7%
of it · the rest is predicted
WITH ONE MORE SITE
44% → 69%
of route covered
Mingyue Tang · David Alcantara · Ishan Bansal
AgWireless '26 · ARA COTS RAN, Ames IA

## Slide 2
the gap
Measurements alone cannot site a tower
Same ground, same scale, same colours. Only the coverage differs.
What we measured
What the twin predicts
42%
of samples had no serving cell
938
of 8,176 cells hold a measurement
0
candidate sites the van visited
7,144 samples · 117 km of road · a 178 km² box

## Slide 3
approaches
Four ways to fill in the map
Each one reads something different about the same ground.
Baseline
Fit a curve to the measurements and read it off anywhere.
Ray tracing
Rebuild the terrain and buildings, then trace the signal through it.
Deep learning
Feed it the ground profile along each link and let it learn the rest.
PINN
Learn what distance alone cannot explain, with physics as a rule.
Same ground, four different bets about what matters
Distance, geometry, the shape of the ground, or whatever is left over. Each is cheap to believe until you move it somewhere new.

## Slide 4
results
In sample is not the same as somewhere new
RSRP error in dB. Lower is better. Same rows, same splits, same 200 m buffer between train and test.
Chart: 
| PINN | Deep learning | Baseline | Ray tracing
on data it has seen | 5.63 | 8.56 | 7.35 | 7.61
somewhere new | 15.83 | 13.13 | 9.66 | 7.95
Grey is in sample. Teal is held out by region. The distance between a pair is how much of the score was memory.
Ray tracing barely moves
7.61 dB in sample, 7.95 held out. It is the only model that does not care whether it has seen the ground before.
The learned models memorise
A terrain profile is nearly a unique location label — its nearest neighbour sits 12 m away on the ground. Feed the operator profiles from the wrong links and it scores 13.16 dB against 13.13 with the right ones. It never used the terrain.
Held out by region · 200 m buffer between train and test

## Slide 5
the planner
Turning a surface into a decision
Score 627 candidate sites against 4,731 demand cells — then move every assumption and watch where the answer goes.
Predict
a value in every 200 m cell
→
Define served
eight definitions, one threshold
→
Score
route-km and area gained
→
Constrain
power, access, structures, backhaul
How far the recommended site moves when you change one assumption
Chart: 
| what counts as served | asset class | propagation model | threshold | route vs area
km | 4.24 | 3.35 | 2.06 | 1.28 | 1.21
The definition beats the physics
Changing what counts as service moves the site twice as far as changing the model. It was chosen, not measured.
A neighbourhood, not a pin
Requiring grid power within 1 km moves it 11 km. The exact site repeats in 10% of draws; 3 km in 99%.
198 combinations of model, asset, criterion, threshold and weighting

## Slide 6
demo
The planner, live
The brief's demo artifact: place an asset and immediately see coverage, performance, uncertainty and route benefit change.
map scale ▬ 2 km · ▪ one 200 m demand cell
Rural Coverage Planner
APPROACH
Baseline — fitted physics ▾
WHAT COUNTS AS SERVED
Availability ▾
TARGET
≥ 50% of the time
ROUTE VS AREA
0.70 / 0.30
ASSET
Macro · 37 m · 0 dB
Find the best site
ROUTE-KM
51.9 → 80.5
SCORE
0.421 → 0.652
Heatmap of the chosen criterion over shaded relief, with the drive test drawn on top in a contrasting hue — which doubles as the road network. Amber is the existing tower, the ring is the placement. Three sweep buttons re-solve across every criterion, every weighting and every approach; a constrained variant adds the five buildability layers.
Runs in a browser. No server, no install, no network.